## Slide 1: Neural Spectrospatial Filter
DeLiang Wang
(Joint work with Ke Tan and Zhong-Qiu Wang)
Perception & Neurodynamics Lab
Ohio State University

## Slide 2: Outline
Background
  DNN based binaural speech separation
  Masking based beamforming
Complex spectral mapping approach to speech dereverberation and speaker separation
Neural spectrospatial filter
Notes: 2

## Slide 3: DNN based approach
Jiang et al. (2014) first proposed DNN classification of binaural features for reverberant speech enhancement
  Interaural time difference (ITD) and interaural level difference (ILD)
Using binaural features to train a DNN classifier to estimate the IBM (ideal binary mask)
  Monaural features are also used
With reasonable sampling of spatial configuration, the classifier generalizes well to untrained configurations and reverberation conditions

## Slide 4: Combining spatial and spectral analyses
More recently, Zhang & Wang (2017) used a more sophisticated set of spatial and spectral features
  Separation is based on IRM (ideal ratio mask) estimation
  Spectral features are extracted after fixed beamforming
  Substantially outperform conventional beamformers

## Slide 5: Masking based beamforming
Beamforming as a spatial filter needs to know the target direction for steering purposes
Steering vector typically relies on direction-of-arrival estimation of the target source, or source localization
However, sound localization in reverberant, multi-source environments itself is difficult
  For human audition, localization seems to depend instead on separation (Darwin’08)

## Slide 6: Masking based beamforming (cont.)
A more recent idea uses monaural time-frequency (T-F) masking to guide beamforming (Heymann et al.’16; Higuchi et al.’16)
  Supervised masking helps to specify the target source
  Masking helps also by suppressing interfering sound sources

## Slide 7: MVDR beamformer
To explain the idea, examine the MVDR beamformer
  MVDR (minimum variance distortionless response) aims to minimize the noise energy from nontarget directions while maintaining the energy from the target direction
Array signals can be written as
  and denote the spatial vectors of the noisy speech signal and noise at frame and frequency
  : speech or target source
  : received speech signal by the array
  : steering vector of the array

## Slide 8: MVDR beamformer (cont.)
We can solve for an optimal weight vector
  denotes the conjugate transpose
  is the spatial covariance matrix of the noise
As the minimization of the output power is equivalent to the minimization of the noise power:

## Slide 9: MVDR beamformer (cont.)
The enhanced speech signal (MVDR output) is
  Hence, the accurate estimation of and is key
  corresponds to the principal eigenvector of , the spatial covariance matrix of speech
With speech and noise uncorrelated, we have
  A noise estimate is crucial for beamforming performance, just like in traditional speech enhancement

## Slide 10: Masking based beamforming
A T-F mask provides a way to more accurately estimate noise (and speech) covariance matrix from noisy input
  Heymann et al. (2016) use RNN with LSTM (long short-term memory) for monaural IBM estimation
  Higuchi et al. (2016) compute a ratio mask using a spatial clustering method
  From Erdogan et al. (2016)

## Slide 11: Masking based beamforming (cont.)
Masking based beamforming is responsible for impressive ASR results on CHiME-3 and CHiME-4 challenges
  These results are much better than using traditional beamformers
Masking based beamforming represents a major advance in beamforming based separation and multi-channel automatic speech recognition (ASR)

## Slide 12: Outline
Background
  DNN based binaural speech separation
  Masking based beamforming
Complex spectral mapping approach to speech dereverberation and speaker separation
Neural spectrospatial filter
Notes: 12

## Slide 13: Complex spectral mapping
We have proposed to address multi-channel speech dereverberation using the complex spectral mapping (CSM) approach (Wang & Wang’20)
  Based on the strategy of target cancellation
  Single-channel dereverberation is treated as a special case
Notes: 13

## Slide 14: Multi-channel reverberant recordings
Reverberation corresponds to an infinite number of delayed and attenuated copies of an original sound source
  A dereverberation method needs to also consider diffuse background noise
Direct-path signal
Reflections
Microphone array
Speaker
Reverberant room
Diffuse Noise
Notes: 14

## Slide 15: Signal model for reverberant-noisy speech
For a reverberant -channel mixture in the short-time Fourier transform (STFT) domain
  Y
  : direct-path target signal at reference microphone
  : relative transfer function, or steering vector
  : reflections or reverberations of target signal
  : reverberant background noise
  : mixture signal

## Slide 16: Complex spectral mapping approach
Phase relations of a sound source between multiple microphones encode spatial characteristics
Complex spectral mapping is a natural approach to represent signal phase in addition to magnitude
This approach employs DNN to predict the real and imaginary (RI) parts of the direct sound from the corresponding reverberant-noisy signal
  It uses real-valued DNN to perform complex-domain processing (Williamson et al.’16)
Notes: 16

## Slide 17: Two-channel real and imaginary spectrograms
Real and imaginary spectrograms both exhibit clear speech structure, unlike magnitude and phase spectrograms
  Real and imaginary parts are related by a phase shift
Both microphones, as well as inter-microphone differences, show speech structure
Notes: 17

## Slide 18: Model diagram
Target cancellation strategy first performs speech dereverberation in individual channels using a common DNN
Dereverberated signals are then fed to an MVDR beamformer
The RI parts of the mixture with the beamformed target signal subtracted are used as additional features to further improve speech dereverberation
Reverberant
Room
Single-channel
Dereverberation
Network
Single-channel
Dereverberation
Network
Multi-channel Dereverberation
Network
Target Speech
Noise
…
MVDR
…
…
…
…
Shared parameters
Notes: 18

## Slide 19: Single-channel complex spectral mapping
Predict based on
Loss functions in the RI domain
  Unlike earlier work on anechoic speech enhancement (Williamson et al.’16; Fu et al.’17; Tan & Wang’19), we address speech dereverberation and denoising
  The magnitude (Mag) loss leads to much better speech quality scores while slightly degrading SNR scores, reflecting the relative importance of magnitude
Notes: 19

## Slide 20: MVDR beamforming
Covariance matrix estimation
  Note the difference from mask-based beamforming, which applies a real-valued mask to mixture signals
Steering vector estimation and beamforming
  ;
  extracts the principal eigenvector
Notes: 20

## Slide 21: Multi-channel dereverberation
We feed the RI parts of , as well as the RI parts of , to the second DNN to estimate the RI parts of
  The term corresponds to the filtered version of all nontarget signals
  With an accurate beamformer, the term is close to , hence a highly discriminant feature for dereverberation
  Without this term, DNN may confuse a direct-path signal and its reflections
The second DNN can be viewed as a post-filter
Notes: 21

## Slide 22: REVERB challenge evaluation
Train on simulated RIRs (room impulse responses) and WSJCAM0 speech corpus
Evaluate the trained models, without retraining, on the REVERB challenge dataset (Kinoshita et al.’16)
  Simulated noisy-reverberant utterances using measured RIRs
  Recorded noisy-reverberant utterances
  Eight-microphone circular array with radius fixed at 10 cm
  T60 in the range [0.25, 0.7] s
  Speaker to array distance in the range [0.5, 2.5] m
  Air conditioning noise
Baselines
  Single- and multi-channel weighted prediction error (WPE) method (Nakatani et al.’10) with or without further beamforming
Notes: 22

## Slide 23: Dereverberation results on REVERB test data
Clear improvements over WPE, WPE+WDAS (weighted delay-and-sum beamformer), and WPE+DNN-based MVDR
  Acronyms: CD: cepstral distance; LLR: log likelihood ratio; SRMR: speech-to-reverberation modulation energy ratio
Notes: 23

## Slide 24: ASR results on REVERB real test data
Clear improvements over WPE, WPE+WDAS, and WPE+DNN-based MVDR
  WER: word error rate
Notes: 24

## Slide 25: Sound demo
Test on REVERB recorded utterances
  8-mic circular array with 10 cm radius
  T60 0.7 s
  Speaker to array distance 2.5 m
  Mixture:
  1ch WPE:
  1ch complex spectral mapping:
  8ch WPE+WDAS:
  8ch complex spectral mapping:
Notes: 25

## Slide 26: Multi-channel speaker separation
Major advances are made in monaural talker-independent speaker separation
  Representative approaches: deep clustering (Hershey et al.’16), permutation-invariant training (PIT) (Kolbak et al.’17)
Multi-channel recordings provide a spatial dimension that may further improve separation performance
Notes: 26

## Slide 27: MISO-based architecture
We have proposed a MISO (multi-input and single-output) module, resulting in MISO-BF-MISO architecture (Wang et al.’21)
  TI-MVDR: time-invariant MVDR
  Source alignment through utterance-level PIT
Multi-Channel
Separation
Network (MISO1)
Multi-Channel
Separation
Network (MISO1)
Multi-Channel Enhancement Network (MISO2)
…
…
…
Shared parameters
Multi-Channel
Separation
Network (MISO1)
…
Reverb Room
Speaker 1
Noise
TI-MVDR
Source Alignment across Microphones
…
…
…
Speaker 2
…
…
…
…
…
TI-MVDR
Multi-Channel Enhancement Network (MISO2)
Shared parameters
Notes: 27

## Slide 28: Libri-CSS evaluation
Libri-CSS for continuous speech separation (CSS) contains recorded conversational data by playing LibriSpeech utterances through loudspeakers in a reverberant room (Chen et al.’20)
Baseline models
  A mask-based beamforming method provided with the dataset using the default ASR backend (Chen et al.’20)
  An updated version of the above method with a more powerful end-to-end ASR backend (Chen et al.’20a)
Notes: 28

## Slide 29: Libri-CSS utterance-wise results
Our WER results are better than the strong baselines, particularly with the default ASR backend
  0S and 0L indicate no overlap with short and long inter-utterance silence
Adding magnitude features to RI parts leads to ASR improvements
Notes: 29

## Slide 30: Continuous-input results
Similar profile of results to the utterance-wise case, but worse overall as expected
Adding a trained speaker counting (SC) module yields clearly better ASR results
Notes: 30

## Slide 31: Outline
Background
  DNN based binaural speech separation
  Masking based beamforming
Complex spectral mapping approach to speech dereverberation and speaker separation
Neural spectrospatial filter
Notes: 31

## Slide 32: Motivation and introduction
For a fixed array with stable spatial information, do we really need a beamformer?
In other words, can multi-channel complex spectral mapping fully utilize both spectral and spatial cues?
The answer, we believe, is yes
  All discriminative features are contained in the multi-channel complex spectrograms of a mixed signal
  The complex representation in MC-CSM (multi-channel CSM) naturally encodes inter-channel phase relations
  Single-channel processing is, by definition, a special case
  Let deep learning figure out the most discriminative spectral and spatial features for performing a particular task
  We call this processing neural spectrospatial filtering (Tan et al.’22)
Notes: 32

## Slide 33: Neural spectrospatial filter
The spectrospatial filter operates on the single-channel spectral inputs of individual microphones, as well as inter-channel spatial cues implicitly available through the complex representation
This all-neural approach is conceptually simple and computationally efficient, compared to mask-based beamforming followed by single-channel postfiltering
Notes: 33

## Slide 34: How does the spectrospatial filter perform?
We have systematically evaluated the spectrospatial filter and compared with related approaches using three array geometries
  2-channel linear array
  8-channel linear array
  7-channel circular array
Notes: 34

## Slide 35: Comparison baselines
Oracle delay-and-sum (DS), time-invariant TI-MVDR and time-varying MVDR (TV-MVDR)
  Target direction is provided to DS, or premixed target and interference are used in covariance matrix calculations
Mask-based (MB) TI-MVDR
  DNN is trained to estimate the IRM
CSM-based TI-MVDR (CSM TI-MVDR) and CSM TV-MVDR
  DNN-estimated target and interference are used in covariance matrix calculations
Postfilter (PF) can be added
  DNN is trained to estimate the IRM or complex spectrogram
Notes: 35

## Slide 36: DNN architecture
Diagram of DC-CRN
A RNN with bidirectional LSTM (BLSTM)
Densely-connected convolutional recurrent network (DC-CRN, Tan et al.’21)
Notes: 36
Skip connections from encoder to decoder

## Slide 37: Speech dereverberation
Comparisons of approaches on speech dereverberation (T60: 0.0 – 1.0 s)
Notes: 37

## Slide 38: Sensitivity to fixed array geometry
A 2-channel array is trained for speech dereverbaratoin with the intermicrophone distance of 10 cm, and tested at the matched and mismatched distances
Performance degrades as distance mismatch increases, as expected. But the trained model does not break down

## Slide 39: Speech enhancement with quasi-diffuse noise
Comparisons of approaches on reverberant speech enhancement at -5 dB
Notes: 39

## Slide 40: Speech enhancement with quasi-diffuse noise
Comparisons of single- and multi-channel enhancement at different SNRs
Single-channel processing produces expected monaural enhancement results
For the same array layout (e.g. linear arrays), more channels consistently boast performance
Notes: 40

## Slide 41: Interim summary of results
Postfiltering substantially elevates beamforming results based on T-F masking and CSM
DC-CRN clearly outperforms BLSTM
Traditional beamforming, even with oracle spatial information, is not competitive
Spectrospatial filtering using MC-CSM produces competitive results compared to DNN based beamforming with postfiltering

## Slide 42: Two-talker speaker separation
LBT (location-based training) assigns the speaker with smaller azimuth to the first DNN output layer and the other speaker to the second output layer
LBT resolves permutation ambiguity through naturally available spatial cues, and performs similarly to uPIT
Notes: 42

## Slide 43: Speech enhancement demo
8-channel speech enhancement with quasi-diffuse noise at -5 dB
  Unprocessed:
  MB TI-MVDR (DC-CRN):
  MB TI-MVDR + PF (DC-CRN):
  CSM TI-MVDR + PF (DC-CRN):
  MC-CSM (DC-CRN):
  Clean
Notes: 43

## Slide 44: Summary
A neural spectrospatial filter is proposed for multi-channel speech dereverberation, speech enhancement, and speaker separation
Multi-channel complex spectral mapping is a conceptually simple, computationally efficient, and effective approach
  MC-CSM reduces to monaural CSM when only single-microphone recordings are available, hence treating multi-channel and single-channel processing exactly in the same way
Neural spectrospatial filtering lets deep learning discover most discriminative spectral and spatial features for performing speech separation tasks