## Slide 1: Deep Learning Based Speech Separation
DeLiang Wang
Perception & Neurodynamics Lab
Ohio State University
& Northwestern Polytechnical University
http://www.cse.ohio-state.edu/pnl/

## Slide 2: Outline of presentation
Introduction
Training targets
Features
Separation algorithms
Concluding remarks

## Slide 3: Real-world audition
What?
Speech
  message
  speaker
    age, gender, linguistic origin, mood, …
Music
Car passing by
Where?
Left, right, up, down
How close?
Channel characteristics
Environment characteristics
Room reverberation
Ambient noise
Notes: 3

## Slide 4: Sources of intrusion and distortion
additive noise from
other sound sources
reverberation from
surface reflections
channel distortion
Notes: 4

## Slide 5: Cocktail party problem
Term coined by Cherry
  “One of our most important faculties is our ability to listen to, and follow, one speaker in the presence of others. This is such a common experience that we may take it for granted; we may call it ‘the cocktail party problem’…” (Cherry’57)
  “For ‘cocktail party’-like situations… when all voices are equally loud, speech remains intelligible for normal-hearing listeners even when there are as many as six interfering talkers” (Bronkhorst & Plomp’92)
Ball-room problem by Helmholtz
  “Complicated beyond conception” (Helmholtz, 1863)
Speech separation problem
  Separation and enhancement are used interchangeably when dealing with nonspeech interference
Notes: 5

## Slide 6: Human performance in different interferences
Source: Wang & Brown (2006)
SRT 23 dB difference in Speech Reception
Threshold!
Notes: 6
don’t comment at this point on the effect of competing speakers

## Slide 7: Some applications of speech separation
Robust automatic speech and speaker recognition
Noise reduction for hearing prosthesis
  Hearing aids
  Cochlear implants
Noise reduction for mobile communication
Audio information retrieval

## Slide 8: Traditional approaches to speech separation
Speech enhancement
  Monaural methods by analyzing general statistics of speech and noise
  Require a noise estimate
Spatial filtering with a microphone array
  Beamforming
    Extract target sound from a specific spatial direction with a sensor array
  Independent component analysis
    Find a demixing matrix from multiple mixtures of sound sources
Computational auditory scene analysis (CASA)
  Based on auditory scene analysis principles
  Feature-based (e.g. pitch) versus model-based (e.g. speaker model)
Notes: 8

## Slide 9: Supervised approach to speech separation
Data driven, i.e. dependency on a training set
Born out of CASA
  Time-frequency masking concept has led to the formulation of speech separation as a supervised learning problem
A recent trend fueled by the success of deep learning
Focus of this tutorial
Notes: 9

## Slide 10: Ideal binary mask as a separation goal
Motivated by the auditory masking phenomenon and auditory scene analysis, we suggested the ideal binary mask as a main goal of CASA (Hu & Wang’04)
The idea is to retain parts of a mixture where the target sound is stronger than the acoustic background, and discard the rest
The definition of the ideal binary mask (IBM)
  θ: A local SNR criterion (LC) in dB, which is typically chosen to be 0 dB
  Optimal SNR: Under certain conditions the IBM with θ = 0 dB is the optimal binary mask in terms of SNR gain (Li & Wang’09)
  Maximal articulation index (AI) in a simplified version (Loizou & Kim’11)
  It does not actually separate the mixture!

## Slide 11: IBM illustration

## Slide 12: Subject tests of ideal binary masking
IBM separation leads to large speech intelligibility improvements
  Improvement for stationary noise is above 7 dB for normal-hearing (NH) listeners (Brungart et al.’06; Li & Loizou’08; Cao et al.’11; Ahmadi et al.’13), and above 9 dB for hearing-impaired (HI) listeners (Anzalone et al.’06; Wang et al.’09)
  Improvement for modulated noise is significantly larger than for stationary noise
With the IBM as the goal, the speech separation problem becomes a binary classification problem
  This new formulation opens the problem to a variety of pattern classification methods
Notes: Brungart and Simpson (2001)’s experiments show coexistence of informational and energetic masking.
They have also isolated informational masking using across-ear effect when listening to two talkers in one ear experience informational masking from third signal in the opposite ear (Brungart and Simpson, 2002)
Arbogast et al. (2002) divide speech signal into 15 log spaced, envelope modulated sinewaves. Assign some to target and some to interference: intelligible speech with no spectral overlaps

## Slide 13: Speech perception of noise with binary gains
Wang et al. (2008) found that, when LC is chosen to be the same as the input SNR, nearly perfect intelligibility is obtained when input SNR is -∞ dB (i.e. the mixture contains noise only with no target speech)
IBM modulated noise for ???
Speech shaped noise
Notes: Create a continuous noise signal that match long-term average spectrum of speech
Further approach to divide “speech-spectrum-shaped” noise into number of bands and modulate with natural speech envelopes
However, noise signal too “speech-like” and reintroduce informational masking (Brungart et al. 2004)
Alternatively, use Ideal Binary Mask to remove informational masking
  Eliminate portions of stimulus dominated by the interfering speech.
  Retain only portions of target speech acoustically detectable in the presence of interfering speech

## Slide 14: Deep neural networks
Why deep?
  As the number of layers increases, more abstract features are learned and they tend to be more invariant to superficial variations
  Superior performance in practice if properly trained (e.g., convolutional neural networks)
Deep structure is harder to train
  Vanishing gradients: Error derivatives tend to become very small in lower layers
  Restricted Boltzmann machines (RBMs) can be used for unsupervised pretraining
  However, RBM pretraining is not needed with large training data

## Slide 15: Different DNN architectures
Feedforward networks
  Multilayer perceptrons (MLPs) with at least two hidden layers
    With or without RBM pretraining
  Convolutional neural networks (CNNs)
    Cascade of pairs of convolutional and subsampling layers
    Invariant features are coded through weight sharing
  Backpropagation is the standard training algorithm
Recurrent networks
  Backpropagation through time is commonly used for training recurrent neural networks (RNNs)
  To alleviate vanishing or exploding gradients, LSTM (long short-term memory) introduces memory cells with gates to facilitate the information flow over time

## Slide 16: Part II: Training targets
What supervised training aims to learn is important for speech separation/enhancement
  Different training targets lead to different mapping functions from noisy features to separated speech
  Different targets may have different levels of generalization
While the IBM is first used in supervised separation (see Part IV), many training targets have since been used
Notes: 16

## Slide 17: Different training targets
TBM (Kjems et al.’09; Gonzalez & Brookes’14) is similar to the IBM except that interference is fixed to speech-shaped noise (SSN)
IRM (Srinivasan et al.’06; Narayanan & Wang’13; Wang et al.’14; Hummersone et al.’14)
  S and N denote speech and noise
  β is a tunable parameter, and a good choice is 0.5
  With β = 0.5, the IRM becomes a square root Wiener filter, which is the optimal estimator of the power spectrum

## Slide 18: Different training targets (cont.)
Spectral magnitude mask (Wang et al.’14)
  Y denotes noisy signal
Phase-sensitive mask (Erdogan et al.’15)
  θ denotes the difference of the clean speech phase and noisy speech phase within the T-F unit
  Because of phase sensitivity, this target usually leads to a better estimate of clean speech than the SMM mask

## Slide 19: Complex Ideal Ratio Mask (cIRM)
This mask is defined so that, when applied, it results in clean speech (Williamson et al.’16)
With complex numbers, solve for mask components
  Subscripts r and i denote real and imaginary components
  Some form of compression (e.g. tangent hyperbolic function) should be used to bound mask values

## Slide 20: Different training targets (cont.)
Target magnitude spectrum (TMS) (Lu et al.’13; Xu et al.’14; Han et al.’14)
  A common form of the TMS is the log-power spectrum of clean speech
Gammatone frequency target power spectrum (GF-TPS) (Wang et al.’14)
The estimation of these two targets corresponds to spectral mapping, as opposed to T-F masking for earlier targets

## Slide 21: Signal approximation
In signal approximation (SA), training aims to estimate the IRM but the error is measured against the spectral magnitude of clean speech (Weninger et al.’14)
  RM(t, f) denotes an estimated IRM
  This objective function maximizes SNR

## Slide 22: Illustration of various training targets
Factory noise at -5 dB
(a) IBM (b) TBM (c) IRM (d) GF-TPS
(e) SMM (f) PSM (g) TMS

## Slide 23: Evaluation of training targets
Wang et al. (2014) studied and evaluated a number of training targets using the same DNN with 3 hidden layers, each with 1024 units
Other evaluation details
  Target speech: TIMIT
  Noises: SSN + four nonstationary noises from NOISEX
    Training and testing on different segments of each noise
  Trained at -5 and 0 dB, and tested at -5, 0, and 5 dB
  Evaluation metrics
    STOI: standard metric for predicted speech intelligibility
    PESQ: standard metric for perceptual speech quality
    SNR

## Slide 24: Comparisons
Comparisons among several different training targets
  An additional comparison for the IRM target with multi-condition (MC) training of all noises (MC-IRM)
Comparisons with different approaches
  Speech enhancement (SPEH) (Hendriks et al.’10)
  Supervised NMF: ASNA-NMF (Virtanen et al.’13), trained and tested in the same way as supervised DNN separation

## Slide 25: STOI comparison for factory noise

## Slide 26: PESQ comparison for factory noise

## Slide 27: Summary among different targets
Among the two binary masks, IBM estimation performs better in PESQ than TBM estimation
Ratio masking performs better than binary masking for speech quality
  IRM, SMM, and GF-TPS produce comparable PESQ results
SMM is better than TMS for estimation
  Many-to-one mapping in TMS vs. one-to-one mapping in SMM, and the latter should be easier to learn
  Estimation of spectral magnitudes or their compressed version tends to magnify estimation errors

## Slide 28: Part III: Features for supervised separation
For supervised learning, features and learning machines are two key components
Early studies only used a few features
  ITD/ILD (Roman et al.’03)
  Pitch (Jin & Wang’09)
  Amplitude modulation spectrogram (AMS) (Kim et al.’09)
Subsequent studies expanded the list
  A complementary set is recommended: AMS+RASTA-PLP+MFCC (Wang et al.’13)
  A new feature, called MRCG (multi-resolution cochleagram), is found to be discriminative (Chen et al.’14)

## Slide 29: A systematic feature study
Extending Chen et al. (2014), Delfarah and Wang (2017) recently conducted a feature study that considers room reverberation and both speech enhancement and speaker separation
  Evaluation done at the low SNR level of -5 dB, with implications for speech intelligibility improvements

## Slide 30: Evaluation framework
Each frame of features is sent to a DNN to estimate the IRM

## Slide 31: Features selected for evaluation
Features examined before include GF (gammatone frequency), GFCC (Shao et al.’08), GFMC, AC-MFCC, RAS-MFCC, PAC-MFCC, PNCC (Kim & Stern’12), GFB, and SSF
In addition, newly studied ones include
  Log spectral magnitude (LOG-MAG)
  Log mel-spectrum (LOG-MEL)
  Waveform signal (WAV)

## Slide 32: STOI improvements (%)

## Slide 33: Result summary
Best performing features are MRCG, PNCC, and GFCC under different conditions
Gammatone-domain features (MRCG, GF and GFCC) perform strongly
Modulation-domain features do not perform well
Waveform signal without any feature extraction is not a good feature
The most effective feature sets:
  PNCC, GF, and LOG-MEL for speech enhancement
  PNCC, GFCC, and LOG-MEL for speaker separation

## Slide 34: Part IV. Separation algorithms
Monaural separation
  Speech-nonspeech separation
  Speaker separation
  Separation of reverberant speech
Multi-channel separation
  Spatial feature based separation
  Masking based beamforming
Notes: 34

## Slide 35: Early monaural attempts at IBM estimation
Jin & Wang (2009) proposed MLP-based classification to separate reverberant voiced speech
  A 6-dimensional pitch-based feature is extracted within each T-F unit
  Classification aims at the IBM, but with a training target that takes into account of the relative energy of the T-F unit
Kim et al. (2009) proposed GMM-based classification to perform speech separation in a masker dependent way
  AMS features are extracted within each T-F unit
  First monaural speech segregation algorithm to achieve speech intelligibility improvement for NH listeners

## Slide 36: DNN as subband classifier
Y. Wang & Wang (2013) first introduced DNN to address the speech separation problem
  DNN is used for as a subband classifier, performing feature learning from raw acoustic features
  Classification aims to estimate the IBM

## Slide 37: DNN as subband classifier

## Slide 38: Extensive training with DNN
Training on 200 randomly chosen utterances from both male and female IEEE speakers, mixed with 100 environmental noises at 0 dB (~17 hours long)
  Six million fully dense training samples in each channel, with 64 channels in total
Evaluated on 20 unseen speakers mixed with 20 unseen noises at 0 dB
DNN based classifier produced the state-of-the-art separation results at the time

## Slide 39: Speech intelligibility evaluation
Healy et al. (2013) subsequently evaluated the classifier on speech intelligibility of hearing-impaired listeners
  A very challenging problem: “The interfering effect of background noise is the single greatest problem reported by hearing aid wearers” (Dillon’12)
Two stage DNN training to incorporate T-F context in classification

## Slide 40: Results and sound demos
Both HI and NH listeners showed intelligibility improvements
HI subjects with separation outperformed NH subjects without separation

## Slide 41: Generalization to new noises
While previous speech intelligibility results are impressive, a major limitation is that training and test noise samples were drawn from the same noise segments
  Speech utterances were different
  Noise samples were randomized
This limitation can be addressed through large-scale training for IRM estimation (Chen et al.’16)

## Slide 42: Large-scale training
Training set consisted of 560 IEEE sentences mixed with 10,000 (10K) non-speech noises (a total of 640,000 mixtures)
  The total duration of the noises is about 125 h, and the total duration of training mixtures is about 380 h
  Training SNR is fixed to -2 dB
The only feature used is the simple T-F unit energy (GF)
DNN architecture consists of 5 hidden layers, each with 2048 units
Test utterances and noises are both different from those used in training

## Slide 43: STOI performance at -2 dB input SNR
 | Babble | Cafeteria | Factory | Babble2 | Average
Unprocessed | 0.612 | 0.596 | 0.611 | 0.611 | 0.608
100-noise model | 0.683 | 0.704 | 0.750 | 0.688 | 0.706
10K-noise model | 0.792 | 0.783 | 0.807 | 0.786 | 0.792
Noise-dependent model | 0.833 | 0.770 | 0.802 | 0.762 | 0.792
DNN model with large-scale training provides similar results to noise-dependent model

## Slide 44: DNN as spectral magnitude estimator
Xu et al. (2014) proposed a DNN-based enhancement algorithm
  DNN (with RBM pretraining) is trained to map from log-power spectra of noisy speech to those of clean speech
  More input frames and training data improve separation results

## Slide 45: Xu et al. results in PESQ
With trained noises
With two untrained noises (A: car; B: exhibition hall)
Subscript in DNN denotes number of hidden layers

## Slide 46: Xu et al. demo
Street noise at 10 dB (upper left: DNN; upper right: log-MMSE; lower left: clean; lower right: noisy)

## Slide 47: Part IV. Separation algorithms
Monaural separation
  Speech-nonspeech separation
  Speaker separation
  Separation of reverberant speech
Multi-channel separation
  Spatial feature based separation
  Masking based beamforming
Notes: 47

## Slide 48: DNN for two-talker separation
Huang et al. (2014; 2015) proposed a two-talker separation method based on DNN, as well as RNN (recurrent neural network)
  Mapping from an input mixture to two separated speech signals
  Using T-F masking to constrain target signals
    Binary or ratio

## Slide 49: Network architecture and training objective
A discriminative training objective maximizes signal-to-interference ratio (SIR)

## Slide 50: Huang et al. results
DNN and RNN perform at about the same level
  About 4-5 dB better in terms of SIR than NMF, while maintaining better SDRs and SARs (input SNR is 0 dB)
  Demo at https://sites.google.com/site/deeplearningsourceseparation
Binary masking
Ratio masking
Mixture
Separated
Talker 1
Separated
Talker 2
Talker 1
Talker 2

## Slide 51: Talker dependency in speaker separation
Huang et al.’s speaker separation is talker-dependent, i.e. the same two talkers are used in training and testing
  Speech utterances are different between training and testing
Speaker separation can be divided into three classes
  Talker dependent
  Target dependent
  Talker independent

## Slide 52: Target-dependent speaker separation
In this case, the target speaker is the same between training and testing, while interfering talkers are allowed to change
Target-dependent separation can be satisfactorily addressed by training with a variety of interfering talkers (Du et al.’14; Zhang & Wang’16)

## Slide 53: Talker-independent speaker separation
This is the most general case, and it cannot be adequately addressed by training with many speaker pairs
Talker-independent separation can be treated as unsupervised clustering (Bach & Jordan’06; Hu & Wang’13)
  Such clustering, however, does not benefit from discriminant information utilized in supervised training
Deep clustering (Hershey et al.’16) is the first approach to talker-independent separation by combining DNN based supervised feature learning and spectral clustering

## Slide 54: Deep clustering
With the ground truth partition of all T-F units, an affinity matrix is defined as
  is the indicator matrix built from the IBM. is set to 1 if unit belongs to (or dominated by) speaker , and 0 otherwise
  if units and belong to the same speaker, and 0 otherwise
To estimate the ground truth partition, DNN is trained to produce embedding vectors such that clustering in the embedding space provides a better partition estimate

## Slide 55: Deep clustering (cont.)
DNN training minimizes the following cost function
  is an embedding matrix for T-F units, and each row represents an embedding vector for one T-F unit
  denotes the squared Frobenius norm
During inference (testing), the K-means algorithm is applied to cluster T-F units into speaker clusters
Isik et al. (2016) extend deep clustering by incorporating an enhancement network after binary mask estimation, and performing end-to-end training of embedding and clustering

## Slide 56: Permutation invariant training (PIT)
Recognizing that talker-dependent separation ties each DNN output to a specific speaker (permutation variant), PIT seeks to untie DNN outputs from speakers in order to achieve talker independence (Kolbak et al.’17)
  Specifically, for a pair of speakers, there are two possible assignments, each of which is associated with a mean squared error (MSE). The assignment with the lower MSE is chosen and the DNN is trained to minimize the corresponding MSE

## Slide 57: PIT illustration and versions
Frame-level PIT (tPIT): Permutation can vary from frame to frame, hence needs speaker tracing (sequential grouping) for speaker separation
Utterance-level PIT (uPIT): Permutation is fixed for a whole utterance, hence needs no speaker tracing

## Slide 58: CASA based approach
Limitations of deep clustering and PIT
  In deep clustering, embedding vectors for T-F units with similar energies from underlying speakers tend to be ambiguous
  uPIT does not work as well as tPIT at the frame level, particularly for same-gender speakers, but tPIT requires speaker tracing
Speaker separation in CASA is talker-independent
  CASA performs simultaneous (spectral) grouping first, and then sequential grouping across time
Liu & Wang (2018) proposed a CASA based approach by leveraging PIT and deep clustering
  For simultaneous grouping, tPIT is trained to predict the spectra of underlying speakers at each frame
  For sequential grouping, DNN is trained to predict embedding vectors for simultaneously grouped spectra

## Slide 59: Sequential grouping in CASA
Differences from deep clustering
  In deep clustering, DNN based embedding is done at the T-F unit level, whereas it is done at the frame level in CASA
  Constrained K-means in CASA ensures that the simultaneously separated spectra of the same frame are assigned to different speakers

## Slide 60: Speaker separation performance
Talker-independent separation produces high-quality speaker separation results, rivaling talker-dependent separation results
SDR improvements (in dB)

## Slide 61: Talker-independent speaker separation demos
New pair of male-male speaker mixture
Speaker1 -uPIT
Speaker2 - uPIT
Speaker1 - CASA
Speaker2 - CASA
Speaker1 - clean
Speaker2 - clean
Speaker1 – DC++
Speaker2 – DC++

## Slide 62: Part IV. Separation algorithms
Monaural separation
  Speech-nonspeech separation
  Speaker separation
  Separation of reverberant speech
Multi-channel separation
  Spatial feature based separation
  Masking based beamforming
Notes: 62

## Slide 63: Reverberation
Reverberation is everywhere
  Reflections of the original source (direct sound) from various surfaces
Adverse effects on speech processing, especially when mixed with noise
  Speech communication
  Automatic speech recognition
  Speaker identification
Previous work
  Inverse filtering (Avendano & Hermansky’96; Wu & Wang’06)
  Binary masking (Roman & Woodruff’13; Hazrati et al.’13)

## Slide 64: DNN for speech dereverberation
Learning the inverse process (Han et al.’14)
  DNN is trained to learn the mapping from the spectrum of reverberant speech to the spectrum of clean (anechoic) speech
    Work equally well in spectrogram and cochleagram
  Straightforward extension to separate reverberant and noisy speech (Han et al.’15)

## Slide 65: Learning spectral mapping
DNN
  Rectified linear + sigmoid
  Three hidden layers
  Input: current frames + 5 neighboring frame on each side
  Output: current frame

## Slide 66: Dereverberation
Clean
Reverberant
(T60 = 0.6 s)
Dereverberated

## Slide 67: Two-stage model for reverberant speech enhancement
Noise and reverberation are different kinds of interference
  Background noise is an additive signal to the target speech
  Reverberation is a convolutive distortion of a speech signal by a room impulse response
Following this analysis, Zhao et al. (2017) proposed a two-stage model to address combined noise and reverberation

## Slide 68: DNN architecture
The system has three modules:
  Denoising module performs IRM estimation to remove noise from noisy-reverberant speech
  Dereverberation module performs spectral mapping to estimate clean-anechoic speech
  Time-domain signal reconstruction (TDR) module (Wang & Wang’15) performs time-domain optimization to improve magnitude spectrum estimation

## Slide 69: Results and demo
Average across different reverberation times (0.3 s, 0.6 s, 0.9 s), different SNRs (-6 dB, 0 dB, 6 dB), and four noises (babble, SSN, DLIVING, PCAFETER)
  Recent tests with hearing-impaired listeners show substantial intelligibility improvements
Demo (T60 = 0.6 s, babble noise at 3 dB SNR)
 | STOI (in %) | PESQ
unprocessed | 61.8 | 1.22
masking | 77.7 | 1.81
proposed | 82.6 | 2.08

## Slide 70: Part IV. Separation algorithms
Monaural separation
  Speech-nonspeech separation
  Speaker separation
  Separation of reverberant speech
Multi-channel separation
  Spatial feature based separation
  Masking based beamforming
Notes: 70

## Slide 71: Binaural separation of reverberant speech
Speech separation has extensively used binaural cues
  Localization, and then location-based separation
T-F masking for separation
  Roman et al. (2003) proposed the first supervised method for binaural separation
  DUET (Yilmaz & Richard’04) is the first unsupervised method

## Slide 72: DNN based approach
Jiang et al. (2014) proposed DNN classification based on binaural features for reverberant speech separation
  Interaural time difference (ITD) and interaural level difference (ILD)
Using binaural features to train a DNN classifier to estimate the IBM
  Monaural GFCC features are also used
Systematic examination of generalization to different configurations and reverberation conditions

## Slide 73: Training and test corpus
ROOMSIM is used with KEMAR dummy head
  A library of binaural impulse responses (BIRs) is created with a room configuration: 6m×4m×3m
  Three reverberant conditions with T60: 0s, 0.3s and 0.7s
Seventy-two source azimuths
  Azimuth angles from 0º to 355º, uniformly sampled at 5º, with distance fixed at 1.5m and elevation at zero degree
  Target fixed at 0º
  Number of sources: 2, 3 and 5
Target signals: TIMIT utterances
  Interference: Babble
  Training SNR is 0 dB (with reverberant target as signal)
  Default test SNR is -5 dB

## Slide 74: Generalization to untrained configurations
Two-source configuration with reverberation (0.3s T60)
  HIT stands for the hit rate (compared to the IBM) and FA for the false-alarm rate
  With reasonable sampling of spatial configurations, DNN classifiers generalize well

## Slide 75: Combining spatial and spectral analyses
Recently, Zhang & Wang (2017) used a more sophisticated set of spatial and spectral features
  Separation is based on IRM estimation
  Spectral features are extracted after fixed beamforming
  Substantially outperforming conventional beamformers

## Slide 76: Masking based beamforming
Beamforming as a spatial filter needs to know the target direction for steering purposes
Steering vector is typically supplied by direction-of-arrival (DOA) estimation of the target source, or source localization
However, sound localization in reverberant, multi-source environments itself is difficult
  For human audition, localization depends on separation (Darwin’08)
A recent idea is to use monaural T-F masking to guide beamforming (Heymann et al.’16; Higuchi et al.’16)
  Supervised masking helps to specify the target source
  Masking also helps by suppressing interfering sound sources

## Slide 77: MVDR beamformer
To explain the idea, look at the MVDR beamformer
  MVDR (minimum variance distortionless response) aims to minimize the noise energy from nontarget directions while maintaining the energy from the target direction
Array signals can be written as
  and denote the spatial vectors of the noisy speech signal and noise at frame and frequency
  : Speech source
  : received speech signal by the array
  : steering vector of the array

## Slide 78: MVDR beamformer (cont.)
We solve for an optimal weight vector
  denotes the conjugate transpose
  is the spatial covariance matrix of the noise
As the minimization of the output power is equivalent to the minimization of the noise power:

## Slide 79: MVDR beamformer (cont.)
The enhanced speech signal (MVDR output) is
  Hence, the accurate estimation of and is key
  corresponds to the principal component of , the spatial covariance matrix of speech
With speech and noise uncorrelated, we have
  A noise estimate is crucial for beamforming performance, just like in traditional speech enhancement

## Slide 80: Masking based beamforming
A T-F mask provides a way to more accurately estimate noise (and speech) covariance matrix from noisy input
  Heymann et al. (2016) use RNN with LSTM for monaural IBM estimation
  Higuchi et al. (2016) compute a ratio mask using a spatial clustering method
  From Erdogan et al. (2016)

## Slide 81: Masking based beamforming (cont.)
Zhang et al. (2017) trained a DNN for monaural IRM estimation, and multiple ratio masks are combined into one via maximum selection
  denotes the estimated IRM from the DNN at frame l and frequency f
  An element of the noise covariance matrix is calculated per frame by integrating a window of neighboring 2L+1 frames. Per-frame estimation of is better than over the entire utterance or a signal segment

## Slide 82: Masking based beamforming (cont.)
Masking based beamforming is responsible for impressive ASR results on CHiME-3 and CHiME-4 challenges
  These results are much better than using traditional beamformers
Masking based beamforming represents a major advance in beamforming based separation and multi-channel ASR

## Slide 83: Part V: Concluding remarks
Formulation of separation as classification, mask estimation, or spectral mapping enables the use of supervised learning
Advances in supervised speech separation in the last few years are truly impressive (Wang & Chen’18)
  Large improvements over unprocessed noisy speech and related approaches
  The first demonstrations of speech intelligibility improvement in noise
  Elevation of beamforming performance

## Slide 84: A solution in sight for cocktail party problem?
What does a solution to the cocktail party problem look like?
  A system that achieves human auditory analysis performance in all listening situations (Wang & Brown’06)
An ASR system that matches the human speech recognition performance in all noisy environments
  Dependency on ASR

## Slide 85: A solution in sight (cont.)?
A speech separation system that helps hearing-impaired listeners to achieve the same level of speech intelligibility as normal-hearing listeners in all noisy environments
  This is my current working definition – see my IEEE Spectrum cover story in March, 2017

## Slide 86: Further remarks
Supervised speech processing is the mainstream
  Signal processing provides an important domain for supervised learning, and it in turn benefits from rapid advances in machine learning
Use of supervised processing goes beyond speech separation and recognition
  Multipitch tracking (Huang & Lee’13, Han & Wang’14)
  Voice activity detection (Zhang et al.’13)
  SNR estimation (Papadopoulos et al.’16)
  Localization (Pertila & Cakir’17; Wang et al.’18)

## Slide 87: Review of presentation
Introduction
Training targets
Features
Separation algorithms
  Monaural separation
    Speech-nonspeech separation
    Speaker separation
    Separation of reverberant speech
  Multi-channel separation
    Spatial feature based separation
    Masking based beamforming
Concluding remarks

## Slide 88: Resources and acknowledgments
This tutorial is based in part on the following overview
  D.L. Wang & J. Chen (2018): “Supervised speech separation based on deep learning: An overview” IEEE/ACM T-ASLP, vol. 26, pp. 1702-1726
DNN Matlab toolbox for speech separation
  http://www.cse.ohio-state.edu/pnl/DNN_toolbox
Source programs for some algorithms discussed in this tutorial are available at OSU Perception & Neurodynamics Lab’s website
    http://www.cse.ohio-state.edu/pnl/software.html
Thanks to Jitong Chen, Donald Williamson, Yuzhou Liu, and Zhong-Qiu Wang for their assistance in the tutorial preparation

## Slide 89: Cited literature and other readings
Ahmadi, Gross, & Sinex (2013) JASA 133: 1687-1692.
Anzalone et al. (2006) Ear & Hearing 27: 480-492.
Avendano & Hermansky (1996) ICSLP: 889-892.
Bach & Jordan (2006) JMLR 7: 1963-2001.
Bronkhorst & Plomp (1992) JASA 92: 3132-3139.
Brungart et al. (2006) JASA 120: 4007-4018.
Cao et al. (2011) JASA 129: 2227-2236.
Chen et al. (2014) IEEE/ACM T-ASLP 22: 1993-2002.
Chen et al. (2016) JASA 139: 2604-2612.
Cherry (1957) On Human Communication. Wiley.
Darwin (2008) Phil Trans Roy Soc B 363: 1011-1021.
Delfarah & Wang (2017) IEEE/ACM T-ASLP 25: 1085-1094.
Dillon (2012) Hearing Aids (2nd Ed). Boomerang.
Du et al. (2014) ICSP: 65-68.
Erdogan et al. (2015) ICASSP: 708-712.
Erdogan et al. (2016) Interspeech: 1981-1985.
Gonzales & Brookes (2014) ICASSP: 7029-7033.
Han et al. (2014) ICASSP: 4628-4632.
Han et al. (2015) IEEE/ACM T-ASLP 23: 982-992.
Han & Wang (2014) IEEE/ACM T-ASLP 22: 2158-2168.
Hazrati et al. (2013) JASA 133: 1607-1614.
Healy et al. (2013) JASA 134: 3029-3038.
Helmholtz (1863) On the Sensation of Tone. Dover.
Hendriks et al. (2010) ICASSP: 4266-4269.
Hershey et al. (2016) ICASSP: 31-35.
Heymann et al. (2016) ICASSP: 196-200.
Higuchi et al. (2016) ICASSP: 5210-5214.
Hu & Wang (2004) IEEE T-NN 15: 1135-1150.
Hu & Wang (2013) IEEE T-ASLP 21: 122-131.
Huang & Lee (2013) IEEE T-ASLP 21: 99-109.
Huang et al. (2014) ICASSP: 1581-1585.
Huang et al. (2015) IEEE/ACM T-ASLP 23: 2136-2147.
Hummersone et al. (2014) In Blind Source Separation, Springer.
Isik et al. (2016) Interspeech: 545-549.
Jiang et al. (2014) IEEE/ACM T-ASLP 22: 2112-2121.
Jin & Wang (2009) IEEE T-ASLP 17: 625-638.
Kim & Stern (2012) ICASSP: 4101-4104.
Kim et al. (2009) JASA 126: 1486-1494.

## Slide 90: Cited literature and other readings (cont.)
Kjems et al. (2009) JASA 126: 1415-1426.
Kolbak et al. (2017) IEEE/ACM T-ASLP: 153-167.
Li & Loizou (2008) JASA 123: 1673-1682.
Li & Wang (2009) Speech Comm. 51: 230-239.
Liu & Wang (2018) ICASSP: 5399-5403.
Loizou & Kim (2011) IEEE T-ASLP 19: 47-56.
Lu et al. (2013) Interspeech: 555-559.
Narayanan & Wang (2013) ICASSP: 7092-7096.
Papadopoulos et al. (2016) IEEE/ACM T-ASLP 24: 2495-2506.
Pertila & Cekar (2017) ICASSP: 6125-6129.
Roman & Woodruff (2013) JASA 133: 1707-1717.
Roman et al. (2003) JASA 114: 2236-2252.
Shao et al. (2008) ICASSP: 1589-1592.
Srinivasan et al. (2006) Speech Comm. 48: 1486-1501.
Virtanen et al. (2013) IEEE T-ASLP 21: 2277-2289.
Wang (March 2017) IEEE Spectrum: 32-37.
Wang & Brown, Ed. (2006) Computational Auditory Scene Analysis. Wiley & IEEE Press.
Wang & Chen (2018) IEEE/ACM T-ASLP 26: 1702-1726.
Wang et al. (2008) JASA 124: 2303-2307.
Wang et al. (2009) JASA 125: 2336-2347.
WangY & Wang (2013) IEEE T-ASLP 21: 1381-1390.
WangY et al. (2013) IEEE T-ASLP 21: 270-279.
WangY et al. (2014) IEEE/ACM T-ASLP 22: 1849-1858.
WangY & Wang (2015) ICASSP: 4390-4394.
Wenninger et al. (2014) GlobalSIP MLASP Symp.
Williamson et al. (2016) IEEE/ACM T-ASLP 24: 483-492.
Wu & Wang (2006) IEEE T-ASLP 14: 774-784.
Xu et al. (2014) IEEE Sig. Proc. Lett. 21: 65-68.
Yilmaz & Rickard (2004) IEEE T-SP 52: 1830-1847.
Zhang & Wang (2016) IEEE/ACM T-ASLP 24: 967-977.
Zhang & Wang (2017) IEEE/ACM T-ASLP 25: 1075-1084.
Zhang et al. (2017) ICASSP: 276-280.
Zhang & Wu (2013) IEEE T-ASLP 21: 697-710.
Zhao et al. (2017) ICASSP: 5580-5584.